## Slide 1
BD9B300MUV-E2EVK-101 Measurement Report
August 11, 2014
Hosted by: Xuan Dang & Vu Phan

## Slide 2
Equipment list
Regulated DC Power Supply
  QJE QJ3005XE (0-30V/5A)
Multimeter:
  Fluke 87V True RMS
  Fluke 106
Oscilloscope
  Rigol DS1102E
Electronic Load
  B&K BK8500
Current probe
  RP1001C

## Slide 3
Functional Test
Testing procedure
  Turn on the DC Supply. Set output of the DC Supply in range from 2.7V to 5.5V and turn it off. Connect DC the Supply to: [+]VIN(TP2) and [-]GND(TP3) of evaluation board.
  Connect Electronic Load to: [+]VOUT(TP4) and [-]GND(TP5). Power on Electronic Load, set input of Electronic Load to 3A.
  Set constant on-time and operation mode of device.
  Turn on the DC Supply.
  Turn on load.
  Move header J1 to turn EN on.

## Slide 4
Functional Test (cont.)
Result:
  VIN = 5V
  IOUT = 3A
FREQ (Set by header J2) | MODE (Set by header J3) | VOUT | Result
2.0MHz (FREQ=L) | DSLLM/PWM (MODE=L) | 3.32V | Passed
2.0MHz (FREQ=L) | PWM (MODE=H) | 3.31V | Passed
1.0MHz (FREQ=H) | DSLLM/PWM (MODE=L) | 3.31V | Passed
1.0MHz (FREQ=H) | PWM (MODE=H) | 3.31V | Passed

## Slide 5
Hot Plugging Test
Test condition
  VIN = 5.5V
  IOUT = 3A
  With original diode D1: P4SMA6.8A
Result:
IIN_MAX= 21.4A
VIN peak transient voltage is 7.6V > VIN Maximum Rating (7V)
The IC still operate properly after 100+ test time.
VIN 2V/Div. (DC)
IIN 5A/Div. (AC)

## Slide 6
Circuit Quiescent Current Measurement
Test condition
  VIN = 0-5.5V
  Room temperature 25oC
Chart: VCC (V)
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9000000000000004 | 4 | 4.0999999999999996 | 4.2 | 4.3 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.7 | 4.8000000000000007 | 4.9000000000000004 | 5 | 5.0999999999999996 | 5.2 | 5.3000000000000007 | 5.4 | 5.5
FREQ=L, MODE=L, With LED | 0 | 0.02 | 0.02 | 0.03 | 0.05 | 0.17 | 0.26 | 0.33 | 0.35 | 0.37 | 0.3 | 1.93 | 1.86 | 5.12 | 5.25 | 5.4 | 5.54 | 5.72 | 5.89 | 6.1 | 6.62 | 7.64 | 9.22 | 10.49 | 11.83 | 12.31 | 4.25 | 4.25 | 4.27 | 4.28 | 4.3 | 4.32 | 4.35 | 4.37 | 4.39 | 4.41 | 4.42 | 4.44 | 4.46 | 4.48 | 4.5
FREQ=L, MODE=H, With LED | 0 | 0.02 | 0.02 | 0.03 | 0.05 | 0.17 | 0.26 | 0.33 | 0.35 | 0.37 | 0.38 | 4.52 | 4.84 | 5.11 | 5.25 | 5.38 | 5.54 | 5.71 | 5.88 | 6.09 | 6.5 | 7.8 | 9.06 | 10.33 | 11.92 | 12.3 | 12.49 | 12.8 | 13.08 | 13.44 | 13.74 | 14.05 | 14.4 | 14.73 | 15.02 | 15.3 | 15.64 | 15.97 | 16.29 | 16.62 | 17
FREQ=H, MODE=L, With LED | 0 | 0.02 | 0.02 | 0.03 | 0.05 | 0.17 | 0.26 | 0.33 | 0.35 | 0.37 | 0.5 | 4.06 | 4.31 | 4.45 | 4.56 | 4.7 | 4.8 | 5.01 | 5.18 | 5.33 | 4.16 | 4.02 | 4.04 | 4.04 | 4.06 | 4.09 | 4.11 | 4.14 | 4.16 | 4.18 | 4.21 | 4.25 | 4.25 | 4.27 | 4.3 | 4.32 | 4.33 | 4.36 | 4.38 | 4.41 | 4.42
FREQ=H, MODE=H, With LED | 0 | 0.02 | 0.02 | 0.03 | 0.05 | 0.17 | 0.26 | 0.33 | 0.35 | 0.37 | 0.5 | 1.72 | 4.35 | 4.49 | 4.6 | 4.73 | 4.88 | 5.02 | 5.19 | 5.37 | 6.61 | 7.68 | 7.95 | 8.48 | 8.88 | 9.27 | 9.72 | 10.08 | 10.5 | 10.92 | 11.31 | 11.73 | 12.07 | 12.42 | 12.86 | 13.16 | 13.5 | 13.81 | 14.14 | 14.43 | 14.73

## Slide 7
Efficiency Measurements
Test condition
  VIN = 5V
  VOUT = 3.3V
  With P4SMA6.8A
  Room temperature 25oC
Chart: IOUT (mA)
| 0 | 25 | 50 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400 | 2500 | 2600 | 2700 | 2800 | 2900 | 3000
FREQ=L, MODE=L | 0 | 75.6 | 83.2 | 85.5 | 87.1 | 90.1 | 91.8 | 92.6 | 93.5 | 93.9 | 93.7 | 94 | 94.2 | 94.2 | 94.4 | 94.3 | 94.5 | 94.3 | 94.4 | 94.2 | 94.2 | 94.2 | 94 | 93.8 | 93.8 | 93.8 | 93.5 | 93.3 | 92.4 | 91.6 | 91 | 91.4 | 91.1
FREQ=L, MODE=H | 0 | 51.5 | 67.1 | 80 | 87.1 | 90 | 91.6 | 92.2 | 92.7 | 93 | 93.1 | 93.4 | 94 | 94 | 94 | 93.8 | 93.6 | 93.3 | 93.5 | 93.3 | 93.8 | 93.7 | 93.3 | 93.3 | 93 | 93.9 | 93.5 | 93.3 | 92.7 | 92.4 | 92 | 91.5 | 91.2
FREQ=H, MODE=L | 0 | 82.5 | 86.8 | 91.7 | 93.6 | 94.3 | 95 | 95.1 | 95.2 | 96.3 | 96.2 | 96.1 | 96.4 | 96.7 | 96.6 | 96.3 | 96.7 | 96.4 | 96.4 | 96.7 | 96.8 | 96.6 | 96.3 | 96.5 | 96.1 | 95.6 | 95.1 | 95 | 95.2 | 95.4 | 95.5 | 95.1 | 94.5
FREQ=H, MODE=H | 0 | 55 | 73.3 | 83.5 | 91.7 | 93.8 | 94.6 | 94.8 | 95.4 | 95.9 | 95.8 | 95.8 | 96.8 | 96.7 | 96.7 | 96.4 | 96.1 | 95.9 | 96.4 | 96.3 | 96.8 | 96.5 | 96.4 | 96.8 | 96.6 | 96.3 | 96.1 | 95.8 | 95.4 | 95.8 | 95.6 | 95.2 | 95

## Slide 8
Load Response Measurements
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=0  3A, FREQ=L, MODE=L)
VOUT 100mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 9
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=3A  0, FREQ=L, MODE=L)
VOUT 100mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 10
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=0  3A, FREQ=L, MODE=H)
VOUT 50mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 11
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=3A  0, FREQ=L, MODE=H)
VOUT 50mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 12
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=0  3A, FREQ=H, MODE=L)
VOUT 100mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 13
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=3A  0, FREQ=H, MODE=L)
VOUT 100mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 14
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=0  3A, FREQ=H, MODE=H)
VOUT 50mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 15
Load Response Measurements (cont.)
Load response characteristic
(VIN=5V, VOUT=3.3V, IOUT=3A  0, FREQ=H, MODE=H)
VOUT 50mV/Div. (AC)
IOUT 1.5A/Div. (DC)

## Slide 16
Ripple Response Measurements
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=0, FREQ=L, MODE=L)
VSW 2V/Div. (DC)
VOUT 10mV/Div. (AC)

## Slide 17
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=3A, FREQ=L, MODE=L)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 18
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=0, FREQ=L, MODE=H)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 19
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=3A, FREQ=L, MODE=H)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 20
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=0, FREQ=H, MODE=L)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 21
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=3A, FREQ=H, MODE=L)
VSW 2V/Div. (DC)
VOUT 50mV/Div. (AC)

## Slide 22
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=0, FREQ=H, MODE=H)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)

## Slide 23
Ripple Response Measurements (cont.)
VOUT Ripple voltage
(VIN=5V, VOUT=3.3V, IOUT=3A, FREQ=H, MODE=H)
VSW 2V/Div. (DC)
VOUT 20mV/Div. (AC)